## Slide 1: Tay Valley Township Landfill Master Plan
March 7th, 2017
Maberly
Glen Tay
Stanleyville

## Slide 2: Agenda(s) August 21st VS. 2016 March 7th 2017
Operational Review
Five landfills – Closed sites- Open Sites - Winter Operations – Summer Operations -Waste, Shingles - BB, Metal, Glass, Tires, Reuse, Batteries, C&D, Appliances– Transport of Waste, BB & Other Diversion - Scrap Tonnages 833t Waste 804t Diversion ---- Remaining Capacity - 177000 m3 – 154000m3 - 5900m3 - 45 Years
Strategic Plan – Implications
Remaining Life - Reuse Centre - Yearly Contribution $25000 Closure Costs - Reuse Centre 20 t/y - Weigh Scale - Waste Audit - - Diversion of Organic - Additional Recyclables - Public Education – Environmental Stewardship – Cover Cost – Cost of Waste Streams.
Regulatory Framework – Including Bill 151
EPA – OD legal – Operations Phase 1 of Site - Compliance Issue OR 101/94 50% reduction – High Expectations - OR 232/98 OD surveys - Bill 90 3R waste diversion – MOE Guidelines B7 & B9 Provincial Water Quality Standards. Bill 151 Evolving tonne – Waste Free Ontario – WDO  Authority Producer responsibility
Landfill Financial Model – 3 Segment Model
Model Scenario Outcomes
Baseline, Increased C&D Revenue, Full Utilizations of Compactor, Thursday Only Cover, Two Compactors, Weigh Scale, 10% waste to recycling Roll off IBS – Dedicated Roll-Off for Waste , C&D, Metal , MURF, Waste Diversion Contractor Curb Side Curbside Pickup with Loan and Depreciation
Future Plan(s) & Summary

## Slide 3: Agenda – March 7th, 2017
Cost Savings & Service Delivery Through:
Operational Considerations
Transportation
Curbside Pickup
Increased Service Delivery at Low Cost !

## Slide 4: Landfill Model 3 Segments – Labour Division
Three Segments Model: 1. Waste
2. Blue Box Diversion
3. Non Blue Box Diversion
Direct Labour Allocation 4 (FTEs) Indirect and Manager Allocations 2 FTEs
40% to Landfills

## Slide 5: Landfill Model Baseline
Total Landfill Net Cost $548k/y
  Waste Net Cost $310k/y
    Waste/Tonne $379/t
  Blue Box Net Costs $130k/y
    BB/Tonne $494/t
  Non Blue Box Diversion Net $108k/y
    NBB Diversion/Tonne $193/t

## Slide 6: Operational Changes
Glen Tay Net Savings Unit Savings Additive1 Additive2
Compactor Fully Utilized $8,805/y $8,805/y
One Day Waste Cover $8,800/y $17,600/y
Increase C&D Revenue $24,000/y $41,600/y
Second Compactor $10,800 $43,586/y

## Slide 7: Roll-Off Truck
Roll-Off $150,000 Purchase
  Roll-Off – Waste Transport ($/y)
    Total 7,575
  Roll-Off – Metal and C&D ($/y)
    Total -17,000
    Aggregate Total - 9,400

## Slide 8: Curbside Pickup Examples
Municipal Curbside Approaches
  Drummond North Elmsley
    Contractor Picks Up and Places Waste and Recycling at Municipal Waste Site
    Approximately a $740,000 increase in expenditure to the residents
      $190/Household, shown on tax bills
  Rideau Lakes Township
    Municipal Personnel Pick Up Waste and Two Stream Recycling and Deliver to Municipal Waste Site
    Using side entry trucks

## Slide 9: Curbside Pickup Personnel Considerations
Curbside
  Reallocation of personnel – This is key for Tay Valley!
    Close Stanleyville & Maberly Sites
    Glen Tay open Saturday & Wednesday (Potentially Sunday in the Summer)
    2.5 employees 2080 h/y on trucks
    2 employees 2.4 days/week at Glen Tay
    Alternately the operation can remain Status Quo and two employees can be hired for Roadside costing an additional
    ~$127,000/y

## Slide 10: Curbside Costs
Curbside Pickup
  Debenture purchase of trucks @ $260,000
    Depreciation $26,000/y
    Loan Repayment $33,000/y
    Supplies $20,000/y
    Labour $27,000/y
    Insurance $2,000/y
    Total $108,000/y
    After fully depreciated $75,000/y

## Slide 11: Improvements & Curbside - 2015
Status Quo - net cost - $548,000/yr.
  Capital Cost Yearly Cost
  Operational Improvements $40k - $43,000/y
Transport of Waste, C&D, Metal
  Roll-off for Waste $150k -$38,000/y
  Roll-off for C&D Metal -$55,000/y
Curbside Pickup
  Purchase of trucks $260K $53,000/y
  Ramp $50k $66,000/y
  Bins $60k $83000/y
  2.50 $/bag -$180,000/y
  Net Cost after Curbside … $401,000/y
  $147,000 reduction in overall net cost.

## Slide 12: Improvements & Curbside - 2018 Increases in Wages, Lifts and Decrease in Bags by 20%
Status Quo - net cost - $568,000/yr. Yearly Cost
  Operational Improvements - - $47,000/y
Transport of Waste, C&D, Metal
  Roll off for Waste $160,000 -$39,000/y
  Roll off for C&D Metal fuel-maint’ -$55,000/y
Curbside Pickup
  Purchase of Trucks $250,000 $51,000/y
  Ramp $50,000 $65,000/y
  Bins $60,000 $81,000/y
  2.50 $/bag -$119,000/y
  Net Cost after Curbside … $449,000/y
  $119,000 reduction in net cost.

## Slide 13: Conclusions
Curbside Pickup – Significant Increase in Service Delivery
RFP/Tender – Recycling
  Roll-Off as Provisional Item of Tender/RFP
Flat Fees for C&D Waste
Second Compactor at Glen Tay Waste Site
Continue to Shave Costs of MOECC Monitoring
  Municipally Shared Hydrogeologist
Reinstate Organic Home Composting Program
Reuse Centre – Icon of the Community

## Slide 14: Curbside Summary
Curbside Pickup
  Provides necessary service to the aging population and attractive service to busy families
    Long term risk to not have curbside in place
  Environmentally responsible
    2 trucks rather than 1000s of cars/wk
  Major increased service delivery to the community as a whole.
  THE END